## Slide 1: Flash-based SSD

## Slide 2: Overview
Solid-state storage device
  No mechanical or moving parts like HDD.
  Built out of transistors (like memory and processors).
  Retain information despite power loss unlike typical RAM.
NAND Flash based SSD
  To write to a given chunk of it, you first have to erase a bigger chunk.
  The number of erase/write is limited.

## Slide 3: Storing Bit
Single-level cell (SLC): a single bit per cell
Multi-level cell (MLC): two bits per cell
Triple-level cell (TLC): three bits per cell
QLC, PLC
Flash memory
cell

## Slide 4: Structure of Flash
Data area
Spare area
Page
Block
typical size:
128KB, 256KB
typical size:
2KB, 4KB
“Spare area" is reserved for bad block mark and ECC values

## Slide 5: Structure of Flash SSD

## Slide 6: Basic Operations
Read : in page unit
Write(program): 1  0: in page unit.
Erase: 0  1: in block unit
1
1
1
1
1
1
1
1
1
1
0
0
1
1
0
0
1
1
0
0
0
0
0
0
1
1
1
1
1
1
1
1
Write 0xCC
(11001100)
Write 0xF0
(11110000)
Erase block
Initial status
Initial status
Can’t write
write
Erase
Block
Block
Block
1010101010101
1010101010101
1111111111111
1010001011101
1010001011101
1111111111111
1111111111111
0000101110100
1111111111111
1111111111111
1111111111111
1111111111111

## Slide 7: Performance of Flash
Raw Flash Performance Characteristics
Device | Read (us) | Program (us) | Erase (us)
SLC | 25 | 200-300 | 1500-2000
MLC | 50 | 600-900 | ~3000
TLC | ~75 | ~900-1350 | ~4500

## Slide 8: Reliability of Flash
Wear out
  Flash cells wear out as we program/erase it.
  Finally the block becomes unusable.
  Typical erase/wear out cycle
    MLC-based block: 10,000 P/E (Program/Erase)
    SLC-based block: 100,000 P/E
Disturbance
  When accessing a particular page within a flash, it is possible that some bits get flipped in neighboring pages.
  It is called read disturbance or program disturbance.

## Slide 9: Out-of-place update in Flash memory
Flash memory should be erased before written.
Flash SSD uses out-of-place update for write operation.
sector 0
sector 2
sector 3
sector 4
sector 5
sector 0
sector 1
sector 2
sector 3
sector 4
sector 5
write sector 1
sector 0
sector 1
sector 2
sector 3
sector 4
sector 5
write sector 1
sector 1
1
Block 1
Block 1
Block 1
In-place
out-of-place
sector 1

## Slide 10: Flash Translation Layer
A software that make the SSD look HDD.
  Address translation
    Program pages within an erased block in order (from low page to high page)
  Wear leveling
    FTL should try to spread writes across the blocks of the flash
    Ensuring that all of the blocks of the device wear out at roughly the same time.
  Garbage collection
Applications
Flash Memory
File System
FTL (Flash Translation Layer)
FTL

## Slide 11: Hard Disk and Flash SSD
+
Device Driver
Read
Write
Erase
File System
Read Sectors
Write Sectors
Flash Memory
Flash Memory
Mismatch!
+
Device Driver
Read Sectors
Write Sectors
File System
Read Sectors
Write Sectors

## Slide 12: Flash Translation Layer
Append the write to the next free spot in the currently-being-written-to block

## Slide 13: Direct Map
Logical page N physical page N
A write to logical page N is costly
  read in the entire block
  erase it
  program it
Reliability
  rapidly wearing out if system metadata is repeatedly overwirtten

## Slide 14: Example
Assume that a page size is 4 Kbyte and a block consists of four pages
Write(page number)
  Write(100) with contents a1
  Write(101) with contents a2
  Write(2000) with contents b1
  Write(2001) with contents b2
The initial state of SSD, with all pages marked INVALID(i)

## Slide 15: Example
Erase block 0.
Program pages in order and update mapping information.
After performing four writes.

## Slide 16: Garbage collection
Update the existing page  old version of data becomes obsolete.
Update blocks 100 and 101 with contents c1 and c2.
The pages 0 and 1 in block 0 is old version data and these are called garbage.
These garbage pages must be reclaimed for new writes to take place.
Garbage

## Slide 17: Address Translation
Page 29
Block 125
Map
(#125, #29)
Sec #3045
write
Page 29
Block 125
Page 4
Block 237
Map
(#237, #4)
Sec #3045
Not Used
Block 125
Page 4
Block 237
update

## Slide 18: Garbage collection
The process of finding garbage blocks and reclaiming them
Basic process
  Find a block that contains one or more garbage pages.
  Read in the live(non-garbage) pages from that block.
  Write out those live pages to the next writable pages.
  Reclaim the entire block for use in writing.

## Slide 19: Garbage collection
Update request
for existing data
Block (A)
Find a free page, and
save the new data
Block (A)
New Data
Invalid
This scenario may continue until
there are not enough free blocks
Block (A)
Invalid
Block (B)
Invalid
Block (C)
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Collect valid pages into a free block
Block (A)
Invalid
Block (B)
Invalid
Block (C)
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Invalid
Update the map table, and
erase invalid (obsolete) blocks
Block (A)
Block (B)
Block (C)

## Slide 20: Garbage collection
Garbage collection is expensive
  Require reading and rewriting of live data.
  Ideal garbage collection is reclamation of a block that consists of only dead pages.
Cost of Garbage Collection
  Amount of data blocks that are migrated.
  Overprovision the device by adding extra flash capacity Cleaning can be delayed.
  Run the GC in the background.

## Slide 21: Mapping Table Size
Size of page-level mapping table is too large
  With a 1TB SSD with a 4byte entry per 4KB page, 1GB of DRAM is needed for mapping.
Some approaches to reduce the costs of mapping
  Block-based mapping
  Hybrid mapping
  Page mapping plus caching

## Slide 22: Block Mapping
Mapping at block granularity.
  To reduce the size of a mapping table.
Small write problem
  When a small write occurs, the FTL must read a large amount of live data from the old block and copy them into a new one.
Example
  Logical pages 2000, 2001, 2002, and 2003 are at the same chunk (chunk number = 500), and have different offsets (0, 1, 2, and 3).
  The FTL records that chunk 500 maps to block 0
Notes: Small write problem: 因为是按照Block为单位来管理Mapping映射关系，即便只有一个Page需要写（small write），也需要整个块做拷贝移动，否则，Mapping关系变了，还是Live的Logical Pages就找不到了。所以，要“搬家”就要整个Block一起“搬家”

## Slide 23: Block Mapping Example
If the logical block 2002 is updated with contents c’,
  FTL must read in 2000, 2001, and 2003.
  Write out all four pages in a new location.
  Update the mapping table.

## Slide 24: Hybrid mapping
In hybrid mapping, FTL maintains
  Log blocks: page mapped
  Data blocks: block-mapped
When looking for a particular logical block, the FTL will consult the page mapping table and block mapping table in order.
valid
valid
valid
valid
Write!
Data is written to
the log block
Data Block
Log Block
Notes: With this approach, the FTL keeps a few blocks erased and directs all writes to them; these are called log blocks. Because the FTL wants to be able to write any page to any location within the log block without all the copying required by a pure block-based mapping, it keeps per-page mappings for these log blocks.

## Slide 25: Example
In the following situation,
Update these pages (with data a’, b’, c’, and d’).  write them to the log block. FTL updates the page mapping information.

## Slide 26: Merge
valid
valid
valid
valid
valid
valid
valid
valid
Data Block
Log Block
Free Block
When log block is full, perform merge.
Free blocks

## Slide 27: Switch Merge
When log block is full, perform merge
  Switch merge

## Slide 28: Switch merge
valid
valid
valid
valid
valid
valid
valid
valid
Free blocks
Data Block
Data Block
Log Block

## Slide 29: Partial Merge
Client overwrites logical block 1000 and 1001 partially. What happened?
The FTL writes logical block 1000 and 1001(contents a’ and b’) to the available pages in new block.
And then, the FTL appends other live data.

## Slide 30: Partial merge
valid
valid
valid
valid
valid
valid
valid
valid
Data Block
Log Block
Free Block
Free blocks

## Slide 31: Switch and Merge

## Slide 32: Page mapping plus caching
Caching only the active part of the page-mapped FTL in memory.
  If a given workload only accesses a small set of pages, the translations of those pages will be stored in the in-memory FTL.
Performance will be excellent without high memory cost.
Cache miss overhead exists.
Page mapping table
Memory
1000 → 0
1001 → 1
1002 → 2
1003 → 3
1004 → 4
1005 → 5
Working set

## Slide 33: Wear Leveling
Erase/Write cycle is limited in Flash memory.
If EW cycle is skewed, that shortens the lifespan of the entire Flash storage.
All blocks should wear out at roughly the same time.
A block may consist of cold data.
  The FTL must periodically read all the live data out of such blocks and re-write it elsewhere.
  Wear leveling increases the write amplification of the SSD and decreases performance.
Sample Policy: Each Flash Block has EW cycle counter.
  Maintain |Max(EW cycle) – Min(EW cycle)| < e
  Maintain |Max(EW cycle) – Min(EW cycle)|/Max(EW cycle) < e
X
O

## Slide 34: Summary
Flash-based SSDs are becoming a common presence in …
  laptops, desktops, and servers inside the datacenters.
Flash Translation Layer
  Address Translation
  Wear Leveling
  Garbage Collection